## Slide 1: TARS Instructions
Screws Needed:
6 M20
40 M14
76 M10

## Slide 2
Chassis Lower (v9)
Chassis Upper (v9)
Chassis Connector Screen Support
M3 20MM x4

## Slide 3
608 Bearing
(metal or Printed)
Arm Spring Divider
(left and Right)
Arm Suspension Mount
x2

## Slide 4
Assembly from previous step x2
Arm Suspension Mount x8

## Slide 5
Upper Strut Mount x2
Spring x2
Secondary Axle x2

## Slide 6
Reinstall

## Slide 7
Secure the 12 ch PWM board to the wall with 4 M2*4 screws (use a flat tip by hand)
Connect the 6v out wires to the
Secure the 12v to 6v Buck convertor with 2 M3*10 screws

## Slide 8
Insert the USB MIC into the RPI
(Not shown here)
Insert the RPI and secure with 4 M2*4 screws. DO NOT OVER TIGHTEN OR USE LONGER SCREWS

## Slide 9
Attach a METAL !!! (unable to print it WILL strip) 25T Aluminum Servo Horn with M3 Threads to the servo using supplied hardware.
Attach upper connecting rod arm with M3*12 screw like arrow shown
“5 Pack ShareGoo 25T Aluminum Servo Horns M3 Threads Metal Steering Arm for RC Car Truck Buggy Airplane-Black”

## Slide 10: IMPORTANT STEP!!!!!!!
Connect Servos to the Servo Controller:
Attach the center servo to the first set of pins on the servo controller (Pin 0).
Connect the robot's left (port) arm to the next set of pins (Pin 1).
Connect the robot's right (starboard) arm to the following set of pins (Pin 2).
Connect the PWM Servo Controller to the Raspberry Pi:
Use the servotester.py script to determine the minimum and maximum PWM values the servo can operate within.
Calculate the dead center value (midpoint) between the minimum and maximum PWM values.
Manually attach the arms at the midpoint position to ensure proper alignment.
Update the Configuration File:
Add the determined center PWM value as neutral to the config.ini file. Add 50 to neutral for up and subtract 50 for down limits.
Center the Arms Mechanically:
Using the servo test tool, set each arm's servo channel to a midpoint value, such as 350 (between the typical range of 100-600).
Detach the arms, reposition them to align mechanically with the center position, and then reattach them.
This ensures the arms are mechanically centered at the specified midpoint value (e.g., 350). For example if you set 350 they should be vertical and perfectly straight.
Calibrate the Center Servo:
Set the center servo to its lowest position (e.g., 88) using the servo test tool.
Reposition and reattach the center servo to align with the lowest point.
Define this position (e.g., 88) as UPHEIGHT in the config.ini file.

## Slide 11
x2
Press in the 608 bearing (metal or printed) in the Arm Left / Right Mount

## Slide 12
Servo Horn Screw
Arm Upper Servo Horn
Servo
x2
Connect servo to RPI first, the PORT and STARBOARD servos should go in pin 1 and 2 (the first pin is 0).

## Slide 13
M3 14MM x4
Arm Upper Servo Horn
Servo
x2
*Rotate the servo to align the bolts

## Slide 14
M3 14MM x4
Arm Upper Servo Horn
Servo
x2
*Rotate the servo to align the bolts

## Slide 15
Insert secondary Axle main lifting rod into center servo.

## Slide 16
Slide the Left arm mount in
Slide in upper rod and screw into place.
Repeat process on
right side

## Slide 17
Rotate main arms and slide in center servo rod assembly.

## Slide 18
Slide on main body mounts

## Slide 19
Rotate entire assembly into place
Secure sides with m4*10 screws

## Slide 20
Slide Arm assembly up and attach
Center servo bracket.

## Slide 21
Each arm is assembly like the picture
x2